## Slide 1: WireCAD E nterprise N etwork T racking

## Slide 2: Remember

## Slide 3: Agenda Day 1
Discuss Concepts
Discuss Structure
UI Tour
Global Database Tour
Equipment Creation Exercise
Cable Type Creation Exercise
Lunch
Backbones Discussion
Backbone Creation Exercise
Backbone Import Discussion
Backbone Import Exercise

## Slide 4: Agenda Day 2
Circuits Discussion
Circuits Exercise
Blind Patch Discussion
Blind Patch Exercise
Lunch
GPS Tools Discussion
Map Tool Locations Exercise
Site Plan Discussion
Site Plan Geo-reference
Site Plan Locations
Site Plan Isometric Discussion

## Slide 5: Agenda Day 3
Site Plan Isometric Exercise
Reports Discussion
Reports Preview Exercise
Report Filtering Exercise
Wrap-up

## Slide 6: Remember The F1 Key Opens The Help File

## Slide 7: Help File Structure
XLT/PRO Topics
ENT Topics
REFERENCE
F1

## Slide 8: Concept 50,000ft View
Enter Data
Visualize
Output CAD/Reports

## Slide 9: Concept 10,000ft View
Create Equipment Definition
Create Cable Types
Create SysNames
Create Backbones
Create Circuits
Visualize
Output
Generate Reports
Global Database
Project Database
Import Backbone Data
Enter Blind Patch Data
Discover and Make Circuits

## Slide 10: What’s a SysName?
SysName Concept Ad
MUX-01 @ Location A
MUX-01 @ Location A
Same Device
MUX-01 @ Location B
MUX-01 @ Location B
Same Device
Different Devices – SysName/Location Pair Differ
Manual Section: 2.1.10

## Slide 11: What’s a SysName?
Each SysName has one and only one corresponding record in the Equipment List

## Slide 12: What’s a Backbone?
Panel Name/Location/Manu/Model
SysName
Panel Name/Location/Manu/Model
SysName
Backbone Number/Type/Quantity
Manual Section: 3.2.1

## Slide 13: What’s a Backbone?
Each Backbone is represented by one record for every strand of fiber or every logical unit of copper

## Slide 14: What’s a Circuit?
Backbone
Jumper
Jumper
Field End Equipment
Head End Equipment
Manual Section: 3.2.3

## Slide 15: What’s a Circuit?
Circuits are represented in the database by a One-to-Many relationship of the Circuit to its Cables (Jumpers/Backbones).

## Slide 16: What’s a Visualization?

## Slide 17: Database Structure
Project Database
Backbones,
Cables,
Equipment,
Circuits, Etc.
Project Database
Backbones,
Cables,
Equipment,
Circuits, Etc.
Project Database
Backbones,
Cables,
Equipment,
Circuits, Etc.
Project Database
Backbones,
Cables,
Equipment,
Circuits, Etc.
Project Database
Backbones,
Cables,
Equipment,
Circuits, Etc.
Global Database
(Common to All Projects)
Manufacturers,
Equipment,
Cable Types, Etc.
SQL Server
WireCAD Desktop Application

## Slide 18: File Structure
Project Folder
Drawings
Project Databases
Project Folder
Drawings
Project Databases

## Slide 19: Reports Concept
Global
Databases
Project
Databases
*.repx
Retrieves and
formats data
supplied by
the various
databases.
Manual Section: 2.4

## Slide 20: Where Do We Start?
Creating a New Project
Manual Section: 2.1.5

## Slide 21: Where Do We Start?
Let’s Start with the Backbone
Panel Name/Location/Manu/Model
SysName
Panel Name/Location/Manu/Model
SysName
Backbone Number/Type/Quantity
Manual Section: 3.2.1

## Slide 22: Backbones Grid
Manual Section: 3.2.1

## Slide 23: Creating a New Backbone
Prerequisites
Create Panel Equipment Definition in the Equipment Library
Create Multi-core Cable Type
Manual Section: 3.2.1.2

## Slide 24: Creating a New Backbone
Steps
Open the Backbones Grid
Click File>Open
Alternately enter “abs” followed by the [Enter] key, this will open the New Backbone tool.
Manual Section: 3.2.1.2

## Slide 25: Creating a New Backbone
Steps
Select or create the lefthand patch panel
Select or create the righthand patch panel
Select the Cable Type
Select the starting point on the lefthand panel
Select the starting point on the righthand panel
Click [Add and Close]
NOTE: THE RED RECORDS IN THE ABOVE IMAGE INDICATE CONNECTORS ON THE PANEL THAT ARE ALREADY IN USE.
Manual Section: 3.2.1.2

## Slide 26: Creating a New Backbone
Results
Six (6) records are added to the Backbone grid
Manual Section: 3.2.1.2

## Slide 27: Backbone Visualization Tools
Riser Diagram
Manual Section: 3.2.1.3

## Slide 28: Backbone Visualization Tools
Layered Digraph
(Ladder) Diagram
Vertical Lines –
Locations
Horizontal Lines –
Backbones
Manual Section: 3.2.1.3

## Slide 29: Backbone Visualization Tools
Map
Manual Section: 3.2.1.3

## Slide 30: Circuits Concept
Circuit
SRC/DST/NUMBER
Cables
Manual Section: 3.2.3

## Slide 31: Circuits Concept
Circuit
SRC/DST/NUMBER
Jumper
Backbone
Jumper
Backbone
Jumper
In Other Words
Cables
Manual Section: 3.2.3

## Slide 32: Circuits Visualization Tool
Two Strand Circuit Visualization
Manual Section: 3.2.3.2

## Slide 33: Circuits Visualization Tool
Map
Manual Section: 3.2.3.2

## Slide 34: Creating a New Circuit Big Picture
Set the Strand Count
Select the Originating Equipment
Select the Destination Equipment
Add Jumpers and Backbones
Build the Circuit
Manual Section: 3.2.3.6.1

## Slide 35: Creating a New Circuit
Steps
Open the Circuits Grid
Click File>Open
Alternately type “nc” into the command line and click [Enter]. This will open the New Circuits tool.
Manual Section: 3.2.3.6.1

## Slide 36: Creating a New Circuit
Steps
Select your Strand Count:
Select or Create the originating equipment:
Select or Create the destination equipment:
Now Select the first Panel to which you will attach.
Manual Section: 3.2.3.6.1

## Slide 37: Creating a New Circuit
Steps
Select the left hand and right hand ports:
Click [Add Jumper]
Click [Next]
Click [Add Backbone]
Click [Next]
Select the next Panel to which you will attach
Lather, Rinse, Repeat
When you are at the last equipment click [Last] and add the final jumper
Click [Build Circuit]
Manual Section: 3.2.3.6.1

## Slide 38: Alternate: Using the Path Finder
Steps (Proceed with Steps 1-7 First)
Click the [Path Finder] tab
Select the “Last Existing” equipment, or in other words, the last known patch panel.
Click the [Find] button. If routes can be found between the first and last patch panels the list will be populated with proposed cables (jumpers and backbones) to achieve the route.
Select the route number to add to your circuit and click [Add Selected Route to Circuit]
Continue to build the circuit.
Manual Section: 3.2.3.6.2

## Slide 39: Blind Patch Concept

## Slide 40: Creating Blind Patch Big Picture
Create Backbones
Enter Blind Patch Data
Discover and Preview Circuits
If Circuit is found to be complete Make Real
CAD Preview/Report
Manual Section: 3.2.2

## Slide 41: Creating a New Blind Patch
Steps
Open the Blind Patches tool.
Select the SysName from the dropdown to populate the grid.
Select the jumper type (simplex or duplex)
Select the row representing the port we are jumpering to.
Click File>New and select the FromSys SysName or CFE equipment.
Manual Section: 3.2.2.1

## Slide 42: Creating a New Blind Patch
Steps
Enter the port name/number
Click File>Save.
Manual Section: 3.2.2.1

## Slide 43: Make a Circuit from a Blind Patch
Steps
Open the Blind Patches tool.
Select the Discover tab.
Click the [Discover Circuits] menu.
Select the row in the Discovered Circuits grid to preview.
If the circuit is found to be complete click [Make Circuit].
Manual Section: 3.2.2.3

## Slide 44: GPS and Map Tools Big Picture
Associate Locations to GPS Coordinates
Visualize Backbones Paths
Select Path to See Stats
Map Tool
Site Plan Drawing
Associate Locations to GPS Coordinates
Visualize Backbones Paths
Select Path to See Stats
Geo-reference Drawing
Manual Section: 3.2.5

## Slide 45: Map Tool
Manual Section: 3.2.5.1

## Slide 46: Site Plan Drawing
Manual Section: 3.2.5.2

## Slide 47: Previewing Reports
Steps
From the Project Explorer, double-click the report *.repx file that you wish to preview.
The report will auto-generate and display unless the report has parameters that the user must enter before the report is generated; in which case, enter the requested data and click [Submit].
Manual Section: 2.4.1

## Slide 48: Common Paths
VISTA / 7 / 8 / 10: Executables: C:\Users\Public\Documents\WireCAD\WireCADx\bin
Shared Program Files: C:\Users\Public\Documents\WireCAD\WireCADx
User Data: C:\Users\YOUR_USER_NAME\AppData\Local\WireCAD\WireCADx