## Slide 1: WireCAD v8 Training
  Fast Track to
  Enlightenment,
  World Peace and
  General “Real Guy”-ness

## Slide 2: Remember!!!
The F1 key opens the on-line help file.
Also check out the WireCAD wiki @ www.wirecad.com/wiki or from within WireCAD click Help>WireCAD wiki.

## Slide 3: Agenda Day 1
Get all the way through a small
one-drawing project, soup to nuts.

## Slide 4: Agenda Day 2
Fill in the holes we skipped over on Day 1
Notes: Notes

## Slide 5: About the Author
Christian Holbrook, President Holbrook Enterprises, Inc.
Christian has had a long and diverse career in the entertainment electronics industry.
Christian served as the chief engineer of several production, postproduction, and broadcast facilities.
Christian served recently as Director of Engineering for the Fox Family Channel.
Christian has owned consulting firms, integration firms and an electronics manufacturing company.
Christian has traded his breadboard for the software development environment and created WireCAD to fill a need many people experience in the system design/integration arena.

## Slide 6: Overview
What for?

## Slide 7: Installation Pictures

## Slide 8: Recent Installations

## Slide 9: Installation Pictures

## Slide 10: Installation Pictures
© 2010 Holbrook Enterprises, Inc. All Rights Reserved

## Slide 11: System Drawings

## Slide 12: System Databases

## Slide 13: System Reports

## Slide 14: File Based vs. Database
File based documentation relies on a single file or series of files to present data representing system documentation. Examples: Visio, AutoCAD, Excel.
Database based documentation provides a central repository for all of the data in the collection. Examples: Access, Foxpro, SQL Server.
Enter WireCAD - A Marriage of the Two.
Allows the presentation capabilities of the file based approach and the centralization of the database approach.

## Slide 15: File Based vs. WireCAD
Easy to control duplication of system identifiers and cable numbers
Easy to erroneously duplicate system identifiers and cable numbers
Cable numbers can be orphaned causing errors
Data is already aggregated and can easily be reported on.
Difficult to aggregate data for reporting
Allows Global Error Checking
Cannot Perform Global Error Checking
Cable numbers and system names are available to other drawings
Cable numbers and system names are available only to the file
WireCAD
File Based

## Slide 16: Concept
My Current Project
Global
Databases
Report Engine
Project Database
Equipment Library

## Slide 17: Concept
My Current Project
Project Database
Cables Table
(bidirectional connection to drawings)
Equipment List
(bidirectional connection to drawings)

## Slide 18: Global Database (WireCADGlobalEquipment.vdb3) VISTADB (WireCAD_Global_Equipment.mdf) SQL
Global
Database
Equipment
  Inputs
  Outputs
Manufacturers
Signal Types
Connectors
Cable Types
Industry Sectors

## Slide 19: Project Database (YourProjectName.vdb3) VISTADB (YourProjectName.mdf) SQL*
Project
Database
Equipment List (SysNames)
Cables
Locations
Named Paths
Backbones (ENT only)
Circuits (ENT only)
Drawings
Discrepancies
*SQL database names cannot begin with numbers

## Slide 20: Remember!!!
The F1 key opens the on-line help file.
Also check out the WireCAD wiki @ www.wirecad.com/wiki or from within WireCAD click Help>WireCAD wiki.

## Slide 21: Report File Concept *.repx
Global
Databases
Project
Databases
*.repx
Retrieves and
formats data
supplied by
the various
databases.

## Slide 22: CAD Vocabulary
Entity – raw drawing component: lines, circles, rectangles, text, images, etc.
Block, Block, or Block????
  A grouping of entities that can be inserted at multiple locations in the drawing.
  A grouping of entities that represent the inputs and outputs for an electronic device.
  A grouping of entities that represents a terminal block.
  A toddler’s toy.
Insert – An instance of a block (sometimes erroneously referred to as a block)

## Slide 23: CAD Vocabulary continued
Text – raw drawing component: lines, circles, rectangles, text, images, etc.
Attribute
  A Tag/Value pair where the Tag represents a descriptor of the data contained in the Value.
  Attributes behave differently when added to a Block. When outside a block the Tag string is displayed. After inclusion in a block the Value string is displayed.
  Example: An attribute with the Tag set to DoorNo and the Value set to 101 will display DoorNo until included in a Block. Whereupon the Value, 101, will be displayed.

## Slide 24: CAD Vocabulary continued
Jack, Terminal, Pointer – Collectively referred to as “Terminals” within WireCAD.
  Note: The distinction between each terminal type determines programmatic behaviour. For example, inserting a terminal that represents a pointer will cause the program to attempt to link one pointer to another when a pointer is double-clicked.
SysName – Unique system identifier or key field. Format can be defined by user.
CableNo – Cable number that uniquely identifies each cable. Format can be defined by user

## Slide 25: Drawing File
Blocks
Dim
Styles
Layers
Text
Styles
Invisible Drawing Tables
Visible Drawing Tables
Model Space
Paper Space

## Slide 26: Drawing Spaces
The CAD file organizes view into two basic drawing spaces: Model and Paper(2K allows for multiple paper spaces called layouts).
The Model space is where the actual model or drawing is drawn.
The Paper space provides opportunity to lay up different views to print.

## Slide 27: Drawing Spaces

## Slide 28
END

## Slide 29
SysName Concept
MUX-01
MUX-01
Same Device
MUX-01

## Slide 30
SysName Concept Advanced
MUX-01 @ Location A
MUX-01 @ Location A
Same Device
MUX-01 @ Location B
MUX-01 @ Location B
Same Device
Different Devices – SysName/Location Pair Differ

## Slide 31
END

## Slide 32
Why Packup and Go?
  You are getting ready to hand the project off to your client.
  You want to create backups.
  You want to move the project to another machine.

## Slide 33
Project Folder
Packup and Go Process
Global
DB
Project
DB
Drawings
Global
DB
Packup Started
Copy Global db
Sync w/ Global db
Copy drawing
dependencies
Compress Folder

## Slide 34
Project Folder
Unpack SQL databases
Global
DB
Project
DB
Drawings
Global
DB
Packup Started
Sync w/ Global db
Sync w/ Project db
Project
DB SQL

## Slide 35
Project Folder
Unpack VISTADB databases
Global
DB
Project
DB
Drawings
Global
DB
Packup Started
Sync w/ Global db

## Slide 36
To Check-out or Not?
You are given the choice on Packup to Check-out the project. This is typically done with SQL Server projects. The process does not change. The only difference is the project is flagged as checked out and is Read-Only until it is checked back in.

## Slide 37
END

## Slide 38: Database Format Decision
Item | SQL Server | VistaDB
File Based |  | X
Server Based | X | 
Zero Administration |  | X
Portable |  | X
ACID Compliant (atomicity, consistency, isolation, durability) | X | X
Database Size | Theoretically unlimited | Practical limit is based upon machine resources. Loading very large databases will require large system resources.
In Process Processing |  | X

## Slide 39: Database Format Decision

## Slide 40: Database Format Decision
Will I be moving the project from machine to machine? If yes, consider staying file based on the project.
Do I have the chops to manage a SQL Server? If no, stay file based. SQL Server requires care and feeding.
Am I away from my network when I work on WireCAD projects? If you lose connection, WireCAD will become hampered.
Do I really need the speed enhancements? If you are working on projects with hundreds of thousands of cables, SQL Server is a must.

## Slide 41
END

## Slide 42: Common Paths
XP: Executables C:\Program Files\WireCAD7 Shared Program Files C:\Documents and Settings\All Users\Documents\WireCAD\WireCAD7 User Data C:\Documents and Settings\YOURUSERNAME\Local Settings\Application Data\WireCAD\WireCAD7
VISTA / 7 / 8: Executables C:\Program Files\WireCAD7 Shared Program Files C:\Users\Public\Documents\WireCAD\WireCAD7 User Data C:\Users\cbh\AppData\Local\WireCAD\WireCAD7

## Slide 43: Demo Project Path
XP: C:\Documents and Settings\All Users\Documents\WireCAD\WireCAD7\
WireCAD Demo Project\ VISTA / 7 / 8: C:\Users\Public\Documents\WireCAD\
WireCAD7\WireCAD Demo Project\

## Slide 44: MACHINE_ROOM Drawing Path
XP: C:\Documents and Settings\All Users\Documents\WireCAD\WireCAD7\
WireCAD Demo Project\Drawings\Single Lines\MACHINE_ROOM.dwg VISTA / 7 / 8: C:\Users\Public\Documents\WireCAD\
WireCAD7\WireCAD Demo Project\ Project\Drawings\Single Lines\MACHINE_ROOM.dwg

## Slide 45
END

## Slide 46
Library Display Properties Hierarchy
WireCAD Default Settings
Your Saved Project Settings
The Device’s Saved Settings
Only exist if the device has been added to a drawing.
Used if they exist and are not overridden by project preferences
Only exist if you have clicked the button to create them.
Used if no Device settings and if they exist.
Used by default if no project or device level settings exist

## Slide 47
END

## Slide 48: SDI Router